## Slide 1: Scientific Computing on Graphics Processing Units
Nicholas Frontiere
ANL/University of Chicago
SF13

## Slide 2: Overview
GPU vs. CPU
CUDA vs. OpenCL (Briefly)
OpenCL execution and memory framework
GPU Hardware
GPU Coding Obstacles and Solutions
  Lock in Step execution (divergent if’s)
  Memory Latency
  Coalesced Memory
  Bank Conflicts
N-Body Example
Conclusion

## Slide 3: GPU vs. CPU
*D. Kirk & W. Hwu 2010
Notes: ALU=Arithmetic Logic Unit
DRAM=Dynamic Random Access Memory
control unit coordinates the components of a computer system
Cache-Larger caches have better hit rates but longer latency. To address this tradeoff, many computers use multiple levels of cache, with small fast caches backed up by larger slower caches.

## Slide 4: CPU
Follows the “multicore” design of a microprocessor
  Attempt to increase the speed of sequential programs.
  Example Intel i7 processor.
Optimized to handle out of order execution
Retains multilevel cache for quick memory access
Implements sophisticated branch prediction
Multiple cores allow for increased multi-tasking as well as threading
Notes: Out of Order:
Instruction fetch. Instruction dispatch to an instruction queue (also called instruction buffer or reservation stations). The instruction waits in the queue until its input operands are available. The instruction is then allowed to leave the queue before earlier, older instructions. The instruction is issued to the appropriate functional unit and executed by that unit. The results are queued.
In Order:
Instruction fetch.
If input operands are available (in registers for instance), the instruction is dispatched to the appropriate functional unit. If one or more operands are unavailable during the current clock cycle (generally because they are being fetched from memory), the processor stalls until they are available.
The instruction is executed by the appropriate functional unit.
The functional unit writes the results back to the register file.
Intel QuickPath Interconnect (QuickPath, QPI)[1][2][3] is a point-to-point processor interconnect developed by Intel which replaces the front-side bus (FSB) in Xeon,

## Slide 5: GPU
Follows the “many-core” design of a microprocessor
  Maximize throughput of parallel algorithms.
Typically the number of cores doubles with each new generation
  Same is true for CPUs, yet GPU’s have many many more cores.
Throughput of Single Precision has increased dramatically
*http://docs.nvidia.com/
Notes: Throughput=number of instructions executed per unit time.
Here is Fermi Architecture

## Slide 6: Question
Would you rather outsource to a
Low Latency
Good Throughput
High Latency
Low Throughput
Capable Contractor
Grad Student
Notes: Throughput=number of instructions executed per unit time.
GPU = High Throughput with ok latency,
CPU = Ok Througbut with low latency.
Latency=

## Slide 7: Question
BUT what about MORE grad students?
Notes: Throughput=number of instructions executed per unit time.
GPU = High Throughput with ok latency,
CPU = Ok Througbut with low latency.
Latency=

## Slide 8
BUT what about MORE grad students?
Low Latency
Good Throughput
Ok Latency
High Throughput
GPU vs. CPU
Do NOT forget Amdahl’s law
Notes: Throughput=number of instructions executed per unit time.
GPU = High Throughput with ok latency,
CPU = Ok Througbut with low latency.
Latency=

## Slide 10: Take Away
Completely limited by the Serial Fraction!
Examples of GPU accelerated code:
  Matrix multiplication, Graphics, Tabular applications, Visual Reduction, etc.

## Slide 11: OpenCL vs. Cuda
Both languages capable of executing GPU kernels.
CUDA is vendor dependent (Nvidia GPUs)
OpenCL can run on many different heterogeneous platforms (CPU, GPU, DSP, etc)
CUDA is more mature and as a result has highly optimized libraries
OpenCL would be considered a “lower level” language and thus harder to code.
Which to choose?
  Depends on what you want to do, what platforms you want to use, and the targeted users.
Notes: Compute Unified Device Architecture
Open Computing Language (OpenCL) (both commercial and open source)
Open standard for parallel programming on heterogeneous platforms
Digital Signal Processors
Can sacrifice portability to match specifics of CUDA.

## Slide 12: OpenCL Platform Model
Host code (CPU)
  Device Queries and Platform Setups (allows one to use multiple devices)
  Push/pull memory to/from device (GPU)
  Compile and Launch Kernel(s)
  Typically performs the branched logic of the application
Kernel Code (GPU)
  Run on the “Compute unit” (GPU)
  Executed on each thread
  Reads/Writes to Device memory (GPU DRAM)
  Has NO access to Host (CPU) memory
__kernel void addTwoArrays(__global float * arr, __global float* arr2,
__global float * return)
{
return[get_global_id(0)]=arr[get_global_id(0)]
+arr2[get_global_id(0)];
}

## Slide 13
// Create an OpenCL context on first available platform context = CreateContext();
// Create a command-queue on the first device available on the created context commandQueue = CreateCommandQueue(context, &device);
// Create OpenCL program from HelloWorld.cl kernel source program = CreateProgram(context, device, "HelloWorld.cl"); // Create OpenCL kernel kernel = clCreateKernel(program, "hello_kernel", NULL); // Set the kernel arguments (result, a, b) errNum = clSetKernelArg(kernel, 0, sizeof(cl_mem), &memObjects[0]); errNum |= clSetKernelArg(kernel, 1, sizeof(cl_mem), &memObjects[1]); errNum |= clSetKernelArg(kernel, 2, sizeof(cl_mem), &memObjects[2]); size_t globalWorkSize[1] = { ARRAY_SIZE }; size_t localWorkSize[1] = { 1 }; // Queue the kernel up for execution across the array errNum = clEnqueueNDRangeKernel(commandQueue, kernel, 1, NULL, globalWorkSize, localWorkSize, 0, NULL, NULL); // Read the output buffer back to the Host errNum = clEnqueueReadBuffer(commandQueue, memObjects[2], CL_TRUE, 0, ARRAY_SIZE * sizeof(float), result, 0, NULL, NULL);

## Slide 14: OpenCL Kernel Execution
Kernels get executed by threads or “work items.” Each item is assigned a “global index (id)”
These work items are collected as “work groups,” and assigned a “group id” and “local id”
These id’s allow the kernel code to perform thread, group, or global specific tasks.
(0,0)
(0,0)
(0,1)
(0,1)
(0,0)
(0,2)
(0,1)
(0,3)
(0,0)
(0,4)
(0,1)
(0,5)
(0,0)
(0,6)
(0,1)
(0,7)
(1,0)
(1,0)
(1,1)
(1,1)
(1,0)
(1,2)
(1,1)
(1,3)
(1,0)
(1,4)
(1,1)
(1,5)
(1,0)
(1,6)
(1,1)
(1,7)
(0,0)
(2,0)
(0,1)
(2,1)
(0,0)
(2,2)
(0,1)
(2,3)
(0,0)
(2,4)
(0,1)
(2,5)
(0,0)
(2,6)
(0,1)
(2,7)
(1,0)
(3,0)
(1,1)
(3,1)
(1,0)
(3,2)
(1,1)
(3,3)
(1,0)
(3,4)
(1,1)
(3,5)
(1,0)
(3,6)
(1,1)
(3,7)
Local Id
Global Id
0
1
2
3
4
5
6
7
Group Id

## Slide 15: OpenCL Memory Hierarchy
__Global Memory: Available to all work items; high latency fetching (hundreds of cycles).
__Constant Memory: Read only memory, low latency.
__Local Memory: Available to a group of threads, fast fetching
__Private Memory: Available to each thread
Host (CPU) Global Memory: Not accessible to device threads. Needs to be pushed by host code to device. High latency
Global Memory
Global Memory/Constant Memory Cache
Local Memory
Private memory
Private memory
Work Item 1
Work Item N
Work Group 1
Private memory
Private memory
Work Item 1
Work Item N
Work Group M
Local Memory
Host
Device
. . . .
. . . .
. . . .
Notes: SP= Streaming processor
SM=Streaming multi-processor

## Slide 16: GPU Hardware
GPU Hardware
http://www.nvidia.com/content/PDF/kepler/NVIDIA-Kepler-GK110-Architecture-Whitepaper.pdf
Notes: TPC= Texture/Processor Clustors
SP= Streaming Processor, (which cointains a multipy-add unit (MAD)
SM= Streaming multiprocessor
SFU = Special Function Unit
L1 Cache = Larger caches have better hit rates but longer latency. To address this tradeoff, many computers use multiple levels of cache, with small fast caches backed up by larger slower caches. Multi-level caches generally operate by checking the smallest level 1 (L1) cache first; if it hits, the processor proceeds at high speed. If the smaller cache misses, the next larger cache (L2) is checked, and so on, before external memory is checked.

## Slide 17: GPU Hardware
Each Work-Item (thread) is executed on a Stream Processor (SP)
SPs are located on one Stream Multiprocessor (SM or SMX)
  Work-Groups are executed on SM’s, where local memory is provided.
Warp Schedulers execute threads of Work-groups on the SM’s; a common optimization goal is to execute as many “warps” on each SM as possible.

## Slide 18: GPU Execution Model (SIMT)
Work Groups are executed via 32 thread launches (aka Warps)
Warps follow Single Instruction Multiple Threading (i.e. all threads in a warp perform the SAME instruction); Optimization implications, will come back to this.
Multiple warps can be executed concurrently on the same SM, aka “waves.” Keplar GPU’s can execute 4 warps concurrently. However the maximum number of warps will not always launch; Depends on memory , number of threads per warp, number of threads per group, etc.
Tails: If groups are not divisible by warp size, can affect performance.

## Slide 19: GPU Hardware
GPU Hardware
http://www.nvidia.com/content/PDF/kepler/NVIDIA-Kepler-GK110-Architecture-Whitepaper.pdf
Notes: TPC= Texture/Processor Clustors
SP= Streaming Processor, (which cointains a multipy-add unit (MAD)
SM= Streaming multiprocessor
SFU = Special Function Unit
L1 Cache = Larger caches have better hit rates but longer latency. To address this tradeoff, many computers use multiple levels of cache, with small fast caches backed up by larger slower caches. Multi-level caches generally operate by checking the smallest level 1 (L1) cache first; if it hits, the processor proceeds at high speed. If the smaller cache misses, the next larger cache (L2) is checked, and so on, before external memory is checked.

## Slide 20
GPU Hardware
http://www.nvidia.com/content/PDF/kepler/NVIDIA-Kepler-GK110-Architecture-Whitepaper.pdf
Notes: NOTE if groups are too small, say = 32, then 32*16=512 < 2048 and occupancy is ¼.
Hyper-Q: Allows multiple CPU cores to launch work on a single GPU simultaneously
Dymanic Parallelism: Before, everything know prior to kernel launch and returned to CPU. Now kernels can run kernels dynamically. Helps with recursive and data-dependent execution. I.e. CPU can be freed up from tasks, or could use simpler GPU. Grid resolution for example

## Slide 21: GPU obstacle: Shortage of Memory
Copying memory from the host CPU to GPU is a necessary step in all GPU kernel applications.
Unfortunately, GPUs can only store a couple GBs of memory in total; even state-of-the-art Kepler can only hold around 8 GBs. Many applications require more, and as a result employ continuous reading and writing to the GPU. This can typically result in transfer latency performance hits.
Possible solution: Simultaneously copy memory to the GPU while performing calculations on the previous memory transfer.

## Slide 22: Lock-Step Execution
Simple example is a divergent IF statemet:
SIMT ensures that when a warp of threads is launched for a work-group and encounters the above statement, both branches are executed (BAD).
Two Solutions:
  A) DON’T DO IT!
  B) Make the branched logic modulo warp size.
  Regardless should play around with group size
  If(get_local_id (0) < 4) {
  Do something
  } else {
  Do something else
  }

## Slide 23: Memory Latency
Fetching global memory requires many latency cycles (~ hundreds), and a result is one of the biggest performance hits.
Local Memory on the other hand has much less latency cycles (~tens) but can have bank conflicts (described later)
Solutions:
  A) Hide latency with arithmetic calculation; while threads are waiting for a memory transfer other warps can be launched to do calculations. Depends on algorithm.
  B) Do one copy from global to local memory and use the local memory speed to distribute the data. Can make use of Coalesced memory. NOTE: Global memory has GBs of data, whereas the local memory per SM has KBs. Very important to proceed this way if original fetch was going to be non-coalesced.
__kernel void addTwoArrays(__gloabl float * arr, __global float* arr2,
__global float * return)
{
return[get_global_id(0)]=arr[get_global_id(0)]
+arr2[get_global_id(0)];
}

## Slide 24: Coalesced Memory Transfer
If memory is accessed non-contiguously, memory fetches will be performed sequentially (BAD if from global memory)
If desired memory fetches are coalesced, the GPU can perform them all at once (modulo half warp size).
Threads (id)
Memory
Newly Allowed

## Slide 25: Bank Conflicts
To avoid multiple global memory latencies, one can copy data to Local Memory for quick access. However, Local Memory is fetched with banks.
Banks contain 4 bytes (Fermi) or 8 bytes (Kepler) of memory.
GPUs typically contain 32 banks per SM
If threads access different memory elements, then all fetches occur at maximum speed (GOOD). Otherwise, fetches are sequential (BAD). Exception: Broadcast to all threads is fast, can be very powerful
4-8 bytes
Broadcast
Notes: So one int or float or double per bank.

## Slide 26: NVDIA OpenCL Visual Profiler
Can profile kernel execution time, as well as host data transfer time.
Can analyze memory bandwidth and instruction issue rate.
Can report number of coalesced loads/stores
Occupancy
  Ratio of active warps per SM to maximum allowed.
  Very informative measure of performance.
Notes: Bandwidth=transfer data over a connection. It is measured as a bit rate expressed in bits per second (bits/s)

## Slide 27: Exemplar: Short Range Force Solver
Our N-body PM solver can resolve forces to ~ 3 grid units. We then require a short range solver to increase the resolution.
A simple approach is to perform a brute force O(N2) nearest neighbor calculation (within radius of 3 cells) utilizing an accelerator such as a GPU (The P3M Method).
One could also use a tree method to reduce computation. We currently have employed such an algorithm, but is not currently accelerated.
The Brute Force method is a simple algorithm which combined with the GPU performance enchantment techniques discussed has proven to be a factor of 4-5 faster then the CPU tree code.
NOTE: GPU code runs at approximately the same speed most redshift.

## Slide 28
imagine a cube of data
divide it into slabs

## Slide 29
~3 grid units

## Slide 30
imagine a GPU

## Slide 40
Keep Repeating

## Slide 44
~3 grid unit cube

## Slide 64
Keep Repeating

## Slide 69: Optimization checklist:
Memory Shortage:
  Algorithm only requires slabs of data, not the entire cube.
Lock-step execution:
  As all particles in a group (chaining mesh) perform the same instruction -- calculate force from neighboring meshes -- there is no divergent logic within a work group.
Global Memory Latency:
  Each thread caches one particle from neighboring mesh into local memory; (thus only one fetch per particle per group not per thread!)
Coalesced Memory Fetching?
  Yes. As particle order does not matter for each mesh bin calculation, each thread can do a local cache sequentially, further reducing latency.
Bank Conflicts:
  Use broadcast from local memory as group of threads need to fetch the same particles.
✔
✔
✔
✔
✔

## Slide 70: Conclusion
GPU acceleration gains are completely determined by serial fraction of the algorithm.
OpenCL allows one to use any heterogeneous platform vs. CUDA which is a more mature but vendor specific language.
Multiple GPU specific considerations
  Memory Storage
  Lock-step execution
  Global memory latency
  Coalesced memory fetching
  Bank Conflicts
Profilers exist to aid you in determining performance
Question? nfrontiere@gmail.com

## Slide 71: OpenACC
Similar to OpenMP, utilized directives
Perhaps a good first step toward attempting acceleration.
With every higher level language, one loses sophistication
Example: Matrix Multiplication
!$acc kernels
do k = 1,n1
do i = 1,n3
c(i,k) = 0.0
do j = 1,n2
c(i,k) = c(i,k) + a(i,j) * b(j,k)
enddo
enddo
enddo
!$acc end kernels